## Slide 1: Challenges in Analyzing Real-Time Systems
Problems in real-time scheduling require either excessive practical constraints to be solved or are NP-complete or NP-hard:
1. When there are mutual exclusion constraints, it is impossible to
find a totally on-line optimal run-time scheduler.
2. The problem of deciding whether it is possible to schedule a set
of periodic processes that use semaphores only to enforce
mutual exclusion is NP-hard.
3. The multiprocessor scheduling problem with two processors, no
resources, arbitrary partial-order relations, and every task
having unit computation time is polynomial.
A partial-order relation indicates that any process can call itself (reflexivity), if process A calls process B, then the reverse is not possible (anti symmetry), and if process A calls process B and process B calls process C, than process A can call process C (transitivity).

## Slide 2: Challenges in Analyzing Real-Time Systems
4. The multiprocessor scheduling problem with two processors, no
resources, independent tasks, and arbitrary computation
times is NP-complete.
5. The multiprocessor scheduling problem with two processors, no
resources, independent tasks, arbitrary partial order, and task
computation times of either 1 or 2 units of time is NP-
complete.
6. The multiprocessor scheduling problem with two processors,
one resource, a forest partial order (partial order on each
processor), and each computation time of every task equal to
1 is NP-complete.
7. The multiprocessor scheduling problem with three or more
processors, one resource, all independent tasks, and each
computation time of every task equal to 1 is NP-complete.

## Slide 3: Challenges in Analyzing Real-Time Systems
8. Earliest deadline scheduling is not optimal in the
multiprocessing case.
9. For two or more processors, no deadline scheduling
algorithm can be optimal without complete a priori
knowledge of deadlines, computation times, and task
start times,
Most multiprocessor scheduling problem are in NP, but for deterministic scheduling this is not a major problem because a polynomial scheduling algorithm can be used to develop an optimal schedule if the specific problem is not NP-complete.
In these cases, alternative, off-line heuristic search techniques can be used. These off-line techniques usually only need to find feasible schedules, not optimal ones.

## Slide 4: Analysis of Round-Robin Systems
Assume that a round-robin system is such that there are n processes in the ready queue, no new ones arrive after the system starts, and none terminate prematurely.
The release time is arbitrary, although all processes are ready at the same time, the order of execution is not predetermined, but is fixed.
Assume all processes have maximum end-to-end execution time, c. Suppose that each process, i, has a different maximum execution time, ci .
Then letting c = max{c1, . . . , cn} yields a reasonably upper bound for the system performance and allows the use of this model.

## Slide 5: Analysis of Round-Robin Systems
Let the time slice be q.
Each process, would get 1/n of the CPU time in chunks of q time units, and each process would wait no longer than (n − 1)q time units until its next time up.
Since each process requires at most c/q time units to complete, the waiting time will be
(n − 1)q c/q so,

## Slide 6: Analysis of Round-Robin Systems
Suppose that there is only one process with a maximum execution time of 500 ms and that the time quantum is 100 ms. Thus, n = 1, c = 500, q = 100, and
which, is as expected.
Suppose there are five processes with a maximum execution time of 500 ms. The time quantum is 100 ms. Hence, n = 5, c = 500, q = 100, which yields
This is intuitively pleasing, since it would be expected that five consecutive tasks of 500 ms each would take 2500 ms end-to-end to complete.

## Slide 7: Analysis of Round-Robin Systems
If there is a context switching overhead, o Now each process still waits no longer than (n − 1)q until its next time quantum, but there is the additional overhead of n·o each time around for context switching.
Again, each process requires at most c/q time quanta to complete. So the worst-case turnaround time for any task is now at most
An assumption is that there is an initial context switch to load the first time around.

## Slide 8: Analysis of Round-Robin Systems
To illustrate, suppose that there is one process with a maximum execution time of 500 ms. The time quantum is 40 ms and context switch time is 1 ms. Hence, n = 1, c = 500, q = 40, o = 1. So,
which is expected since the context switch time to handle the round-robin clock interrupt costs 1 ms each time for the 13 times it occurs.
Suppose that there are six processes, each with a maximum execution time of 600 ms, the time quantum is 40 ms, and context switch time costs 2 ms. Now, n = 6, c = 600, q = 40, and o = 2. Then
which again is pleasing, because one would expect six processes of 600 ms in duration to take at least 3600 ms, without context switching costs.

## Slide 9: Analysis of Round-Robin Systems
In terms of the time quantum, it is desirable that q < c to achieve “fair” behavior.
For example, if q is very large, the round-robin algorithm is just the first-come, first-served algorithm in that each process will execute to completion, in order of arrival, within the very large time quantum.
This also useful for cooperative multitasking analysis or any kind of “fair” cyclic scheduling with context switching costs.

## Slide 10: Response-Time Analysis for Fixed-Period Systems
In general, utilization-based tests are not exact and provide good estimates for a very simplified task model.
A necessary and sufficient condition for schedulability based on worst-case response time calculation:
For the highest-priority task, its worst-case response time evidently will be equal to its own execution time.
Other tasks running on the system are subjected to interference caused by execution of higher-priority tasks.
For a general task τi , response time, Ri, is given as
Ri = ei + Ii
    where Ii is the maximum amount of delay in execution, caused by higher priority tasks, that task τi is going to experience in any time interval [t, t + Ri).
At a critical instant Ii will be maximum, that is, the time at which all higher-priority tasks are released along with task τi .
Consider a task τj of higher priority than τi .Within the interval [0,Ri ), the time of release of τj will be Ri/pj

## Slide 11: Response-Time Analysis for Fixed-Period Systems
Each release of task τj is going to contribute to the amount of interference τi is going to face, and is expressed as:
Each task of higher priority is interfering with task τi. So,
where hp(i) is the set of higher-priority tasks with respect to τi .
Substituting this value in Ri = ei + Ii yields
Due to the ceiling functions, it is difficult to solve for Ri . Without getting into details, a solution is provided where the function R is evaluated by rewriting it as a recurrence relation
where Rni is the response in the nth iteration.
To use the recurrence relation to find response times, it is necessary to compute Rn+1i iteratively until the first value m is found such that
is then the response time Ri . It is important to note that if the equation does not have a solution, then the value of Ri will continue to rise, as in the case when a task set has a utilization greater than 100%.

## Slide 12: Response-Time Analysis: RMA Example
Calculation of response-time analysis for a fixed-priority scheduling scheme
Consider the task set to be scheduled rate monotonically, as shown below:
The highest priority task τ1 will have a response time equal to its execution time, so R1 = 3.
The next highest priority task, τ2 will have its response time calculated as follows. First, R2 = 4.
The recursive values following R02 are derived as:
Since, R12 = R22 it implies that the response time of task τ2,R2, is 7.
Similarly, the lowest priority task τ3 response is derived as follows.
First, R03 = 2, then the next values of R3:
Since, R13 = R23 , the response time of the lowest priority task is 9.

## Slide 13: Analysis of Sporadic and Aperiodic Interrupt Systems
A system having one or more aperiodic or sporadic cycles should be modeled as a rate-monotonic system, but with the nonperiodic tasks modeled as having a period equal to their worst-case expected inter-arrival time.
However, if this approximation leads to unacceptably high utilizations, it may be possible to use a heuristic analysis approach.
The calculation of response times for interrupt systems is dependent on a variety of factors like:
  interrupt latency
  scheduling/dispatching times
  context switch times.
Determination of context save/restore times is the same as for any application code.
The schedule time is negligible when the CPU uses an interrupt controller with multiple interrupts.
When a single interrupt is supported in conjunction with an interrupt controller, it can be timed using instruction counting.

## Slide 14: Interrupt Latency
Interrupt latency is a component of response time, and is the period between when a device requests an interrupt and when the first instruction for the associated hardware interrupt service routine executes.
In the design of a real-time system, it is necessary to consider what the worst-case interrupt latency might be.
Typically, it will occur when all possible interrupts in the system are requested simultaneously.
The number of threads or processes also contribute to the worst-case latency.
Real-time operating systems need to disable interrupts while it is processing lists of blocked or waiting threads.
If design of system requires a large number of threads or processes, latency measurements should be performed to check that scheduler is not disabling interrupts for unacceptably long time.

## Slide 15: 1 PERFORMANCE OPTIMIZATION: Compute at Slowest Cycle
Identifying wasteful computation is a preliminary step in reducing code execution time, and hence, CPU utilization.
Many approaches employed in compiler optimization can be used, but other methods have evolved that are specifically oriented toward real-time systems.
All processing should be done at the slowest rate that can be tolerated.
Examples:
Checking a discrete temperature for a large room at faster than 1 second may be wasteful, for temperature typically cannot change quickly owing to thermal inertia.
In the nuclear plant example, a dedicated sensor is used to monitor the temperature, which then issues a high-level priority if any over temperature is detected.

## Slide 16: 2 PERFORMANCE OPTIMIZATION: Scaled Numbers
In computers, integer operations are faster than floating-point ones
This fact can be exploited by converting floating-point algorithms into scaled integer algorithms.
In the scaled numbers, the least significant bit (LSB) of an integer variable is assigned a real number scale factor.
Scaled numbers can be added and subtracted together and multiplied and divided by a constant (but not another scaled number), the results are converted to floating point only at the last step, thus saving considerable time.
Analog-to-digital (A/D) converter converting accelerometer data:
If the least significant bit of the two’s complement 16-bit integer has value 0.0000153 ft/s2, then any acceleration can be represented up to the maximum value of (215 − 1)∗0.0000153 = 0.5013351 ft/s2.
The 16-bit number 0000 0000 0001 011, for example, represents an acceleration of 0.0001683 ft/s2.

## Slide 17: 2 PERFORMANCE OPTIMIZATION: Scaled Numbers
A common practice is to quickly convert the integer number into its floating point equivalent by xf = x · 0.0000153 and then proceed to use it in calculations directly with other converted numbers;
Example:
diff = xf − zf, where zf is a converted floating-point number.
The calculation can be performed in integer form first and then converted to floating point: diff = (x − z) · 0.0000153.
For applications involving the numerous addition and subtraction of like data, scaled numbers can introduce significant savings.
Multiplication and division by another scaled number cannot be performed on a scaled number as those operations change the scale factor.
Accuracy is generally sacrificed by excessive use of scaled numbers.

## Slide 18: 3 PERFORMANCE OPTIMIZATION: Binary Angular Measure
Another type of scaled number is based on the property that adding 180◦ to any angle is analogous to taking its two’s complement , technique called binary angular measurement (BAM).
Consider the LSB of an n-bit word to be 2-(n−1).180 degrees with the most significant bit (MSB) = 180 degrees.
The range of any angle θ represented this way is 0 ≤ θ ≤ 360 − 180 · c degrees.
A 16-bit BAM word

## Slide 19: 3 PERFORMANCE OPTIMIZATION: Binary Angular Measure
For more accuracy, BAM can be extended to two more words. Each n-bit word has a maximum value of 2 - 2-(n−1) · 180◦ = 360◦ − LSB with granularity
2-(n−1)· 180◦ = LSB
Consider the 16-bit BAM word: 0000 0000 10100 110
Its binary angular measurement is 166 · 180◦ · 2-15 = 0.9118◦.
180 90 45 22.5 … … … … … … … … … … 180·2−14 180·2−15
BAM can be added and subtracted together and multiplied and divided by constants as if they were unsigned integers, and converted at the last stage to produce floating-point results. It is easy to show that the overflow condition for BAM numbers presents no problem as the angle simply wraps around to 0. BAM is frequently used in navigation software, robotic control, and in conjunction with digitizing imaging devices.

## Slide 20: Optimizing Memory Usage
In embedded applications or in legacy systems often the real-time systems engineer is faced with restrictions on the amount of memory available for program storage or for scratchpad calculations, dynamic allocation.
Since there is a fundamental trade-off between memory usage and CPU utilization, when it is desired to optimize for memory usage, it is necessary to trade performance to save memory.
It is important to match the real-time processing algorithms to the underlying architecture.

## Slide 21: Optimizing Memory Usage
In the case of the von Neumann architecture, it is helpful to recognize the effects of such features as cache size and pipeline characteristics.
In the case of cache size, the algorithm should be chosen to optimize the cache hit ratio, the percentage of time that data are found in the cache.
In the case of pipelines, increasing the code locality of reference can reduce the amount of deleterious pipeline flushing.

## Slide 22: ANALYSIS OF MEMORY REQUIREMENTS
With memory becoming denser and cheaper, memory utilization analysis has become less of a concern.
Efficient use of memory is important in small embedded systems and air and space applications where savings in size, power consumption, and cost are desirable.
The total memory utilization is typically the sum of the individual memory utilization for each of the memory areas. Suppose that the memory consists of the program, stack, and RAM areas.
MT = MP · PP +MR · PR +MS · PS
      where MT is the total memory utilization, MP,MR, and MS are the memory utilization for the program, RAM, and stack areas, respectively, and PP PR PS are percentages of total memory allocated for the program, RAM, and stack areas, respectively.

## Slide 23: ANALYSIS OF MEMORY REQUIREMENTS
Memory-mapped I/O and DMA memory are not included in the memory-utilization equation , since they are fixed in hardware.
The program area of memory is generally ROM, which contains the executable code of the real-time program, including the operating system and applications software.
In addition, fixed constants can be stored in this area. Here memory utilization is calculated simply by dividing the number of used locations in the program area by the allowable locations.
MP = UP / TP
    where MP is the memory utilization for the program area, UP is the number of locations used in the program area, and TP is the total available locations in the program area.
These numbers are available as output from the linker.

## Slide 24: ANALYSIS OF MEMORY REQUIREMENTS
Although the program instructions may be stored in RAM instead of ROM for increased fetching speed and modifiability, all global variables should be stored in RAM.
The size of this area is determined at system design time but the loading factor for this area is not determined until the application programs have been completed.
In any case, the memory utilization factor can be computed as MR = UR / TR
    where MR, is the memory utilization for the RAM area, UR is the number of locations used in the RAM area, and TR is the total available locations in the RAM area.
These numbers are available as output from the linker.

## Slide 25: ANALYSIS OF MEMORY REQUIREMENTS
For the stack area the memory utilization factor can be computed as
MS = US / TS
      where MS is the memory utilization for the stack area, US is the number of locations used in the stack area, and TS is the total available locations in the stack area.
For example, a computer system has 64 megabytes of program memory that is loaded at 75%, 24 megabytes of RAM area that is loaded at 25%, and 12 megabytes of stack area that is loaded at 50%. The total memory utilization is
v
v
v

## Slide 26: REDUCING MEMORY UTILIZATION
Memory utilization is less of a problem than it has been in the past, but occasionally a system needs to be designed in which the available main memory is small in relation to the program size.
It is expected that this situation will arise more frequently in the future, as ubiquitous and mobile computing applications call for very small processors with tiny memories.
Most of the approaches developed to reduce memory utilization date from a time when memory was at a premium and might violate the principles of software engineering. Thus, they should be used with caution.

## Slide 27: 1 Variable Selection
Memory utilization in one area can be reduced at the expense of another.
For example, all automatic variables (variables that are local to procedures) increase the loading in the stack area of memory, whereas global variables appear in the RAM area.
By forcing variables to be either local or global, one area of memory may be used at the cost of the other, thus balancing the memory load.
Intermediate result calculations that are computed explicitly require a variable either in the stack or the RAM area, depending on whether it is local or global.
The intermediate value can be placed into a register instead by omitting the intermediate calculation.
e.g . discriminant =b*b-4*a*c;
root=(-b+sqrt(discriminant))*0.5/a;
this code could be replaced by
root=(-b+sqrt(b*B-4*a*c)*0.5/a;
This saves one floating-point variable and thus at least 4 bytes of memory.
This eliminates at least one STORE macroinstruction, reducing time loading as well.

## Slide 28: 2 Memory Fragmentation
Memory fragmentation does not impact memory utilization, but it can produce effects resembling memory overloading.
In this case, although sufficient memory is available, it is not contiguous.
Although compaction schemes are available, they are not desirable in real-time systems, they may be necessary in serious cases of memory overutilization